LOG File
31st December 2022
# Install Ubuntu
- Parition the C drive in Windows System.
  - Issue: Since windows C drive has data at the last part of the drive section, disk management tool wasn’t able to make the continuous segment from the end which had sufficient space.
  - Use third party software to do the partition
- Install Ubuntu Jammy (22.04.01)

2nd January 2023
# Install ROS
ROS Neotic is not intented to work on Ubuntu Jammy. Only ROS 2 can be used on Jammy. But e-puck2 requires ROS Neotic as the documentation is tailored for ROS 1.

3rd January 2023
- Install Ubuntu Focal (20.04.05)
  - Wrong Action: Deleted ubuntu by deleting the volume in disk management tool. The Ubuntu entry in Boot record persisted & caused issue while reinstalling
  - Error: OS signature present – while booting from live USB
    Fix: Turn off secure boot
- Run Eclipse
  - Issue: The new volume was mounted as read only.
    - Fix: Re mounted as read write.
  - Issue: File system doesn’t exist.
    - Solution: Search dropped halfway as alternate option was available
    - Alternate option: Clone the repo into the ‘Documents’ folder which is in root partition
- Install ROS (noetic)

4th January 2023
# Setup ROS Node for SLAM
- Setup the ROS Node for SLAM
  - The documentation is for ROS kinetic. Change the package names also to account for noetic (ROS version).
  - Use CPP packages with Bluetooth communication.

5th January 2023
# Practical
- Run and Test SLAM
  - Setup Bluetooth communication in the e-puck2
  - View the MAP and control the e-puck2 using rviz

6th January 2023
- Learn ROS – Documenation from wiki.ros.org
  - Follow the tuturial

9th January 2023
- Learn ROS – Documentation from wiki.ros.org
  - Follow the tuturial
- Create a ROS node to control the e-puck2
  - Move the robot in circles

10th January 2023
- Autonomous navigation
  - Navigate the robot by using the sensor data

NEXT:
- Understand the operation
- Learn ROS
- Learn SLAM
- Document the process

IMU Controlled movement

PID

# Further Explore
- ROS on Docker